## Slide 1: Exterior light check must be done in all three zones completely. Front Side Rear
Clean
Not Damaged
Proper color for their function
Pg 11-11 & 11-12
Lights

## Slide 2
Pg 11-11 & 11-12
Lights

## Slide 3: Steering
Steering Box/Hoses
  Secure, not leaking
  Not missing nuts and bolts
Steering Linkage
  Link, rod, arm from box to wheel not worn or cracked
  Joints and sockets not worn or loose.
  No missing nuts,bolts, cotter key

## Slide 4
1.
2.

## Slide 5: Brake Drums/Linings
Brake Drum:
No cracks, dents, or holes
No contaminates
Brake Linings
Brake linings should not be worn dangerously thin.
Check the brake linings for contaminants, such as grease, oil, etc.

## Slide 7
Suspension:
Springs
Hangers/Bushing
U-Bolts
Shock Absorber
Spring hanger/mount
Cracked or broken hanger
Missing or damaged bushing
Bushing
U-bolt
Broken, loose, missing bolt, u-bolts or other axle mounting parts
Springs
Missing, shifted, cracked, or broken leaf springs
Shock absorber
Secure and no leaks

## Slide 8
Suspension:

## Slide 9: Slack Adjuster-Push rod
Slack Adjuster and pushrod
Securely mounted slack adjuster and pushrod
Bent, broken, loose or missing parts
Adjusted, not move more than 1 inch when pulled by hand

## Slide 11: Brake Chamber/Brake Hoses
Hoses/Lines
Cracked, worn, frayed or leaking from hose and couplings
Connections, coupling fittings, secure not leaking
Brake Chamber
Not leaking, cracked or dented
Mounted securely
No loose or missing clamps

## Slide 13: Coolant Drive Shaft Exhaust Frame
Exhaust
Damage, signs of leaks, rust or carbon soot
Tightly connected and securely mounted no loose clamps
No cracks, holes or severe dents
Drive Shaft
Not bent, cracked or twisted
Couplings or u-joints secure and free of foreign objects
Frame
Cracks, bends, broken welds, holes or other damage to longitudinal frame
Look for loose, cracked, bent, broken or missing cross members
Coolant
Sight glass for level
Or cap if not hot

## Slide 15: Alternator/Water pump/Air Compressor/Power steering unit Belts-Gear
Belts:
½ - 3/4 deflection
No cracks, frays, wear
Gear:
Operates properly
Not damaged, leaking
Mounted securely
Water pump:
Mounted securely
Not damaged
Not leaking
Operates properly
Alternator:
Mounted securely
Not damaged
Wires securely fastened
Operates properly
Power steering unit:
Mounted securely
Not damaged
Not leaking
Operates properly
Air compressor:
Mounted securely
Not damaged
Not leaking
Operates properly

## Slide 16
Belts:
Gear: